## Slide 1: The Modeling of Single-dof Mechanical Systems

## Slide 2
Lagrange equation for a single-dof system:
where:
q: is the generalized coordinate;
T: is the total kinetic energy of the system;
V: is the total potential energy of the system;
L: is the Lagrangian of the system, given by
is the power supplied to the system by motors delivering controlled forces or torques;
Δ: is the dissipation function associated with all dissipative forces in the system.
(1)

## Slide 3
a) Kinetic Energy of the Rigid Body of a Mechanical System Undergoing Planar Motion
where:
is the mass of the ith rigid body;
is the two-dimensional velocity vector of the center of mass of the rigid body with respect to an inertial frame, representing its magnitude;
is the scalar moment of inertia of the rigid body with respect to its center of mass; and is the scalar angular velocity of the ith rigid body with respect to an inertial frame.
T: Kinetic Energy
The kinetic energy of the rigid body can be determined using ….

## Slide 4
b) Kinetic Energy of the Rigid Body of a Mechanical System Undergoing Planar Motion Based on a Fixed Point Oof the Body
where:
is the scalar moment of inertia of the rigid body with respect to a point of the body that is instantaneously fixed to an inertial frame;
is the scalar angular velocity of the rigid body with respect to an inertial frame.
The kinetic energy of the overall system is the sum of the kinetic energies of all r rigid bodies, i.e.,

## Slide 5
The velocity vector of the center of mass of each body and its scalar angular velocity can be always written as linear functions of the generalized speed.
The total kinetic energy of the system takes the form:
where the coefficients and as well as are, in general, functions of the generalized coordinate q. The first term of that expression is quadratic in the generalized speed; the second term is linear in this variable; and the third term is independent of the generalized speed, but is a function of the generalized coordinate and, possibly, of time as well. Moreover, this function of q is most frequently nonlinear, while the second and the third terms of the same expression arise in the presence of actuators supplying a controlled motion to the system.
(2)

## Slide 6: V: Potential Energy
In setting up the Lagrange equations of the system under study, we need an expression for its potential energy. Here, we assume that we have two possible sources of potential energy: elastic and gravitational.
The potential energy due to gravity is a nonlinear function of the generalized coordinate q, i.e.,
On the other hand, the elastic potential energy is due to springs of all sorts. Hence, the potential energy due to the stiffness of the spring takes the form

## Slide 7
being the elongation or contraction of the spring. The foregoing discussion applies to translational springs, a similar expression applying to torsional springs:
Thus, under the assumption that the system has a total of s springs, the total potential energy is given as
where can be either translational or torsional and is a generalized coordinate.

## Slide 8
Π and D : Power Supplied to a System and Dissipation Function
Single-dof systems have a single generalized force associated with them. If we let the total power developed by force-controlled sources be denoted by , then, the generalized active force associated with the generalized coordinate q is derived as
where is the corresponding generalized velocity.

## Slide 9
Systems are not only acted upon by driving forces but also by dissipative forces that intrinsically oppose the motion of the system.
Here, we postulate the existence of a dissipation function Δ from which the dissipative force is derived as
the negative sign taking into account that Δ is essentially a positive quantity, while opposes motion.
Dissipation of energy occurs in nature in many forms. The most common mechanisms of energy dissipation are:
(a) viscous damping, (b) Coulomb or dry-friction damping,
(c) hysteretic damping,

## Slide 10: The Seven Steps of the Modeling Process
We derive below the general form of the Lagrange equations, Eq. (1), as pertaining to single-dof systems. To this end, we use Eq. (2) to derive the Lagrangian in the form
Hence,
and

## Slide 11
Likewise,
Moreover, the right-hand side of Eq. (1) is nothing but the sum of the terms due to force-controlled sources and dissipation, i.e,
Therefore, the Lagrange equations take the form
In summary, then, the Lagrange equation for single-dof systems takes the form
In summary, the Lagrange equation for single-dof systems takes the form

## Slide 12
the governing model is a second-order ordinary differential equation in the generalized coordinate q.
In this equation, the configuration-dependent coefficient m(q), the generalized mass, while the second term of the left-hand side,
h(q,˙q), contains inertia forces stemming from Coriolis and centrifugal accelerations. For this reason, this term is sometimes called the term of Coriolis and centrifugal forces.
The right-hand side, in turn, is the sum of four different generalized-force terms, namely,
φp(q, t), a generalized force stemming from the potential energy of the Lagrangian;
(2) φm(q, ˙ q, t), a generalized force stemming from motion-controlled sources and contributed by the Lagrangian as well;
(3) φ f (q, ˙ q, t), a generalized force stemming from force-controlled sources, and contributed by the power Π;
(4) φd (q, ˙ q, t), a generalized force of dissipative forces, stemming from the dissipation function Δ.

## Slide 13
Example 1.6.4 from Dynamics Response … by J. Angeles
A Locomotive Wheel Array
Derive the Lagrange equation of the system shown in Fig. This system consists of two identical wheels of mass m and radius a that can be modeled as uniform disks. Furthermore, the two wheels are coupled by a slender, uniform, rigid bar of mass M and length l, pinned to the wheels at points a distance b from the wheel centers. We can safely assume that the wheels roll without slipping on the horizontal rail and that the only nonnegligible dissipative effects arise from the lubricant at the bar-wheel pins. These pins produce dissipative moments proportional to the relative angular velocity of the bar with respect to each wheel.

## Slide 14: A Locomotive Wheel Array
Solution: Under the no-slip assumption, it is clear that a single generalized coordinate, such as θ , suffices to describe the configuration of the entire system at any instant. The system thus has a dof = 1.
We introduce the seven-step procedure to derive the mathematical model sought:
Kinematics
Kinetic energy
Potential energy
Lagrangian
Power supplied
Power dissipation
7. Lagrance Equation

## Slide 15: A Locomotive Wheel Array
Kinematics.
if we denote by P the center of the pin connecting the wheel 1 with the coupler bar, we have
where denotes the relative velocity of P with respect to C1,
C3 has a velocity identical to

## Slide 16: A Locomotive Wheel Array
all that we need to find is
2. Kinetic energy
denotes the moment of inertia of the body about its center of mass
As a matter of fact, will not be needed because body 3 undergoes a pure
translation.

## Slide 17: A Locomotive Wheel Array
whence,

## Slide 18: A Locomotive Wheel Array
3. Potential energy.
We note that the sole source of potential energy is gravity.
4. Lagrangian.
This is now readily derived as
5. Power supplied.
Apparently, the system is not subjected to any force-controlled
source, and hence, = 0.

## Slide 19: A Locomotive Wheel Array
6. Power dissipation.
What is important here is to find the angular velocity of the
bar with respect to each of the wheels
7. Lagrange equation.
Now, all we need is to evaluate the partial derivatives involved in Eq. 1.22, namely,

## Slide 20: A Locomotive Wheel Array
Hence,
and
Furthermore,
the equation sought thus being
Thus, the generalized mass of the system is

## Slide 21: A Locomotive Wheel Array
Likewise, the term of Coriolis and centrifugal forces is readily
identified as
Finally, the right-hand side contains one term of gravity forces, , and one that is dissipative, . The only driving force here is gravity, and this is taken into account in the Lagrangian. We thus have

## Slide 22
Example 1.6.5 from Dynamics Response … by J. Angeles
An Overhead Crane
Now we want to derive the Lagrange equation of the overhead crane of Fig. 1.19 that consists of a cart of mass M that is driven with a controlled motion u(t). A slender rod of length l and mass m is pinned to the cart at point O by means of roller bearings producing a resistive torque that can be
assumed to be equivalent to that of a linear dashpot of coefficient c.

## Slide 23
The rod, undergoes both translation and rotation. Let denote the velocity of the c.o.m of the rod, and ω its scalar angular velocity.
Solution: We proceed as in the foregoing example, in seven steps, namely,
Kinematics
Kinetic energy
Potential energy
Lagrangian
Power supplied
Power dissipation
7. Lagrance Equation
Kinematics
An Overhead Crane

## Slide 24
With regard to , then, at this stage we only set up the velocity triangle of Fig. 1.19. In that triangle, and denote, respectively, the velocity of point O and the relative velocity of C with respect to O. Hence,
2. Kinetic energy. Here, we will need , which is readily obtained from the velocity triangle as
An Overhead Crane

## Slide 25
Now, let and denote the kinetic energies of the cart and the rod, respectively, i.e.,
and hence,
Compared with Eq. 1.27, the foregoing expression yields
An Overhead Crane

## Slide 26
3. Potential energy.
This is only gravitational and pertains to the rod, the potential
energy of the cart remaining constant, and, therefore, can be assumed to be zero. Hence, if we use the level of the pin as a reference,
4. Lagrangian. This is simply
5. Power supplied. Again, we have no driving force, and hence, = 0.
An Overhead Crane

## Slide 27
6. Power dissipation. Here, the only sink of energy occurs in the pin, and hence,
7. Lagrange equations. Now it is a simplematter to calculate the partial derivatives of the foregoing functions:
An Overhead Crane

## Slide 28
In order to complete the Lagrange equations, we need only the generalized force. Since the system is driven under a controlled motion, the active component of the generalized force stems from the Lagrangian, and will be made apparent when we set up the governing equations, the dissipative component being linear in , i.e.,
Therefore, the governing equation becomes
that can be rearranged in the form
An Overhead Crane

## Slide 29
Now we can readily identify the generalized mass as
Likewise,
and so, the system at hand contains neither Coriolis nor centrifugal forces.
An Overhead Crane

## Slide 30
An Overhead Crane
Finally, the right-hand side is composed of three terms: (1) a gravity term that is solely a function of θ , but not of ; (2) a generalized active force that is provided by a motion-controlled source, i.e., the motor driving the cart with a controlled displacement u(t); and (3) a dissipative term. All these terms are displayed below:

## Slide 31
Describe how the mathematical model of Example 1.6.5 changes if the pin is substituted by a motor that supplies a controlled torque , in order to control the orientation of the rod for purposes of manipulation tasks. Here, we assume that this torque is accompanied by a dissipative torque linear in , as in Example 1.6.5.
Example 1.6.6 from Dynamics Response … by J. Angeles
A Force-driven Overhead Crane

## Slide 32
Solution: The motor-supplied torque now produces a power onto the system, the generalized force now containing an active controlled-force component , namely,
all other terms remaining the same. Therefore, the governing equation becomes now
A Force-driven Overhead Crane

## Slide 33
Shown in Fig. is the iconic model of an actuator used to rotate a load—e.g., a control surface in an aircraft, a robot link, a door, or a valve—of mass m, represented by link AB of length a, about a point A. The driving mechanism consists of three elements in parallel, namely, a linear spring of stiffness k, a linear dashpot of coefficient c, and a hydraulic cylinder exerting a controlled force F(t), to lower or raise the load. Under the assumption that the spring is unloaded when s = a, and that the link is a slender rod, find the mathematical model of the foregoing system in terms of θ , which is to be used as the generalized coordinate in this example.
Example 1.6.8 from Dynamics Response … by J. Angeles
A Simplified Model of an Actuator

## Slide 34
Solution: We proceed as in the previous cases, i.e., following the usual seven-step procedure:
A Simplified Model of an Actuator
Kinematics
Kinetic energy
Potential energy
Lagrangian
Power supplied
Power dissipation
7. Lagrance Equation

## Slide 35
1. Kinematics
Besides the foregoing item, we will need a relation between the length of the spring, s, and the generalized variable,θ . This is readily found from the geometry of Fig. 1.21, namely,
2. Kinetic energy.
A Simplified Model of an Actuator

## Slide 36
Thus,
3. Potential energy. We now have both gravitational and elastic forms of potential energy. If we take the horizontal position of AB as the reference level to measure the potential energy due to gravity, then
A Simplified Model of an Actuator

## Slide 37
or, in terms of the generalized coordinate alone,
4. Lagrangian. This is simply
5. Power supplied. The system is driven under a controlled force F(t) that is applied at a speed ˙ s, and hence, the power supplied to the system is
A Simplified Model of an Actuator

## Slide 38
In order to express the foregoing power in terms of the generalized speed , we differentiate the relation between s and θ with respect to time:
thereby obtaining the desired expression:
6. Power dissipation. Power is dissipated only by the dashpot of the hydraulic cylinder, and hence,
A Simplified Model of an Actuator

## Slide 39
7. Lagrange equations. We first evaluate the partial derivatives of the Lagrangian:
where we have written all partial derivatives in terms of angle θ /2. Furthermore,
A Simplified Model of an Actuator

## Slide 40
the equation sought thus being
The generalized mass can be readily identified from the above model as
Also note that the generalized-force terms are identified below as:
while
A Simplified Model of an Actuator

## Slide 41
Finally, the equation of motion can be rearranged as
A Simplified Model of an Actuator

## Slide 42
Shown in Fig. is a highly simplified model of the actuator mechanism of an aircraft control surfacee.g., ailerons, rudder, etc. In the model, a massless slider is positioned by a stepper motor at a displacement u(t). The inertia of the actuator-aileron system is lumped in the rigid, slender, uniform bar of length l and mass m, while all the stiffness and damping is lumped in a parallel spring-dashpot array whose left end A is pinned to a second massless slider that can slide without friction on a vertical guideway. Moreover, it is known that the spring is unloaded when u = l and θ = 0. A second motor, mounted on the first slider, exerts a torque τ (t) on the bar.
Example 1.6.9 from Dynamics Response … by J. Angeles
Motion-driven Control Surface

## Slide 43
(a) Derive the Lagrangian of the system.
(b) Give expressions for the power supplied to the system and for the dissipation function Δ.
(c) Obtain the mathematical model of the system and identify in it the generalized forces (1) supplied by force-controlled sources; (2) supplied by motion controlled sources; (3) stemming from potentials; and (4) produced by dissipation.
Motion-driven Control Surface
Kinematics
Kinetic energy
Potential energy
Lagrangian
5. Power supplied
Power dissipation
7. Lagrance Equation

## Slide 44
Solution:
(a) The kinetic energy of the system is that of the overhead crane of Example 1.6.5, except that now the cart has negligible mass, i.e., M = 0, and hence,
The potential energy is the same as that of Example 1.6.5 plus the elastic energy of the spring, which is
Moreover, from the geometry of Fig. 1.22,
Motion-driven Control Surface

## Slide 45
whence,
and
(b) power supplied and dissipation function Δ.
Motion-driven Control Surface

## Slide 46
and is computed by differentiation of the foregoing expression for s:
(c) mathematical model of the system
Motion-driven Control Surface

## Slide 47
Motion-driven Control Surface

## Slide 48
Thus, the mathematical model is derived as
or,
Motion-driven Control Surface

## Slide 49: Equilibrium States of Mechanical Systems
Henceforth, a mechanical system will be said to be in an equilibrium state if both = 0 and = 0. This condition implies that, at equilibrium, q attains a constant value .
we derive the equilibrium equation in the form

## Slide 50
Find the equilibrium configuration(s) of the system introduced in Example 1.6.5 under the condition that the cart is driven with a constant acceleration .
Example 1.9.1 from Dynamics Response … by J. Angeles
Equilibrium Analysis of the Overhead Crane

## Slide 51
Solution: We first set , and in the governing equation derived in that example, thereby obtaining the equilibrium equation
which can be written as
Equilibrium Analysis of the Overhead Crane

## Slide 52
and hence,
The system, therefore, admits two equilibrium configurations, one with the rod above and one with the rod below the pin.
The foregoing relation among the constant horizontal
acceleration a, the vertical gravity acceleration g and the equilibrium angle is best illustrated in Fig. 1.30, where the force triangle, composed of the pin force , the weight of the rod mg, and the inertia force −ma, is sketched.
Equilibrium Analysis of the Overhead Crane

## Slide 53
Moreover, from Fig. 1.30, it is apparent that
Equilibrium Analysis of the Overhead Crane

## Slide 54
Determine all the equilibrium states of the actuator mechanism introduced in Example 1.6.8.
Example 1.9.2 from Dynamics Response … by J. Angeles
Equilibrium States of the Actuator Mechanism
To this end, assume that

## Slide 55
Solution: Upon setting , , and in the mathematical model derived in Example 1.6.8, the equilibrium equation is obtained as
Equilibrium States of the Actuator Mechanism

## Slide 56
which vanishes under any of the conditions given below:
That is, equilibrium is reached whenever attains any of the three values given below:
Equilibrium States of the Actuator Mechanism

## Slide 57
The foregoing values yield the equilibrium configurations of Fig. 1.31.

## Slide 58
Example 1.9.4 (A System with a Time-varying Equilibrium State). Derive the equilibrium states of the rack-and-pinion transmission of Fig. 1.3.

## Slide 59
Solution: Let us assume that the moment of inertia of the pinion about its center of mass is I, and that its mass is m, its radius being a. Thus, the velocity of its c.o.m is , and hence, the kinetic energy becomes
Moreover, no changes in the potential energy are apparent, since the center of mass of the pinion remains at the same level, and hence, we can set V = 0, which leads to L = T in this case. Now the Lagrange equation of the system is, simply,
and hence, the equilibrium equation, obtained when we set , becomes an identity, namely, 0 = 0.

## Slide 60: Linearization About Equilibrium States. Stability
If a system is in an equilibrium state and is perturbed slightly, then, the system may respond in one of three possible ways:
• The system returns eventually to its equilibrium state
• The system never returns to its equilibrium state, from which it wanders farther and farther
• The system neither returns to its equilibrium state nor escapes from it; rather, the system oscillates about the equilibrium state
In the first case, the equilibrium state is said to be stable or, more precisely, asymptotically stable; in the second case, the equilibrium state is unstable or asymptotically unstable. The third case is a borderline case between the two foregoing cases. This case, then, leads to what is known as a marginally stable
equilibrium state.

## Slide 61
We analyze below a single-dof system governed by the equation
Thus, we denote the value of q at its equilibrium state by and linearize the system about this state, as described below. Moreover, at equilibrium,
First, we perturb slightly the equilibrium state,
Otherwise, one can resort to a series expansion.

## Slide 62
where the subscripted vertical bar indicates that the quantity to its left is evaluated at equilibrium.
At the equilibrium

## Slide 63
An equilibrium configuration is understood throughout the book as a configuration of the system governed by , at which we have assumed that . In evaluating the partial derivatives of h with respect to q and at equilibrium, we have:
Therefore,
substituting
Under the small-perturbation assumption, the quadratic term involving the product ……….
in the left-hand side of the above equation is too small with respect to the linear terms, and hence, is neglected.

## Slide 64
The perturbed equation of motion thus reduces to
with the definitions below:

## Slide 65
Given the linearized equation of a one-dof system,
where mE > 0, the system
• is asymptotically stable if and only if is positive and is non-negative;
• is marginally stable if and only if = 0 and > 0;
• is asymptotically unstable otherwise
we can divide all terms of that equation by
which is the normal form of the second-order ODE governing the motion of the linear system under study, with and , the natural frequency and the damping ratio of the system, respectively, defined as

## Slide 66
For brevity ,we shall write in a simpler form, i.e., by dropping the subscript E and the δ symbol, whenever the equilibrium configuration is either self-understood or immaterial, namely,
or, in normal form, as
with ωn and ζ defined now as
and, obviously, f (t) defined as

## Slide 67
The mathematical model appearing in Eq. 1.57 corresponds to the iconic model of Fig. 1.34.

## Slide 68
A Mass-spring-dashpot System in a Gravity Field

## Slide 69
In Fig. 1.36a the system is displayed with the spring unloaded, while the same system is shown in its static equilibrium position in Fig. 1.36b, this position being that at which the spring force balances the weight of the mass, and hence,
Application of Newton’s equation in the vertical direction now gives
Thus, the equilibrium equation derived above reduces to
Example 1.10.4 (A Mass-spring-dashpot System in a Gravity Field). Illustrated in Fig. 1.36 is a mass-spring-dashpot system suspended from a rigid ceiling. For this system, discuss the difference in the models resulting when the displacement of the mass is measured (a) from the configuration where the spring is unloaded and (b) from the static equilibrium configuration.

## Slide 70
If, rather than measuring the displacement of the mass from equilibrium, we measure it from the position in which the spring is unloaded, then we set up the governing equation in terms of the new variable ξ , defined as
Upon substituting in the governing equation derived above, we have

## Slide 71
Determine the stability of the equilibrium configurations of the overhead crane introduced in Example 1.6.5.
Example 1.10.1 from Dynamics Response … by J. Angeles
Stability Analysis of the Overhead Crane

## Slide 72
which leads to
Solution: In order to undertake the stability analysis of the equilibrium configurations of the system under study, we make the substitutions given below in the governing equation derived in Example 1.6.5, with const and c = 0 (neglect dissipation). We have
Stability Analysis of the Overhead Crane

## Slide 73
We now invoke the assumption that is “small”,
Finally,
We thus have that the equilibrium configuration at which angle lies between and , i.e., the rod-down configuration, is marginally stable. The equilibrium configuration for which lies between and , i.e., the rod-up configuration, is unstable. Note that the natural frequency of the marginally stable configuration is readily derived from the above linearized equation as
Stability Analysis of the Overhead Crane

## Slide 74
Decide whether each of the equilibrium configurations of Fig. 1.31, of the actuator mechanism, found in Example 1.9.2 is stable or unstable, when the system is unactuated—i.e., when F(t) = 0. For the stable cases, whether stability is asymptotic or marginal, and find, in each case, the equivalent natural frequency and, if applicable, the damping ratio.
Example 1.10.2 from Dynamics Response … by J. Angeles
Stability Analysis of the Actuator Mechanism

## Slide 75
Solution: What we have to do is linearize the governing equation about each equilibrium configuration, with F(t) = 0. To do this, we substitute the values below into the Lagrange equation of the system at hand:
The equation of motion thus becomes
We analyze below each of the three equilibrium configurations found in Example 1.9.2:
Stability Analysis of the Actuator Mechanism

## Slide 76
(a : In this case,
the linearized equation about the equilibrium configuration considered here thus becoming, after simplifications,
Stability Analysis of the Actuator Mechanism

## Slide 77
Upon dropping the quadratic terms of the above expression, and rearranging the expression thus resulting in normal form, we obtain
The natural frequency and the damping ratio associated with the linearized system are thus
Stability Analysis of the Actuator Mechanism

## Slide 78
(b) : now we have
Upon substitution of the foregoing values into the Lagrange equation, we obtain, after simplification,
Next, we delete the quadratic terms from the above equation, and rewrite it in normal form, thus obtaining
(c) : this configuration is the mirror-image of the first one,
Stability Analysis of the Actuator Mechanism